## Slide 1
PAST, PRESENT & FUTURE
OF POWER GENERATION
BY H C VERMA
EX-GM, NTPC

## Slide 2: OUTLINE
1.
2.
3.
OVERVIEW OF INDIAN POWER SECTOR
ROLE OF NTPC FOR POWER DEVELOPMENT IN INDIA
FUTURE CHALLENGES OF POWER SECTOR

## Slide 3
INDIAN POWER SECTOR SCENARIO

## Slide 4: POWER SECTOR SCENARIO IN INDIA
INTRODUCTION:-
TODAY EECTRICITY IS A PART AND PARCEL OF OUR DAILY LIFE AND WITHOUT ELECTRICITY WE CAN NOT THINK OF OUR SURVIVAL .
ELECTRICITY IS A FORM OF ENERGY WHICH CAN BE EASILY PRODUCED , EASY TO TRANSPORT, EASY TO USE .
IT IS THE TERMINAL FORM OF ENERGY FOR TRANSMISSION AND DISTRIBUTION.
PER CAPITA ELECTRICITY CONSUMPTION IS ONE OF THE INDEX OF LIVING STANDARD OF PEOPLE OF A PARTICULAR PLACE OR OF A COUNTRY.

## Slide 5
IN BULK QUANTITY ELECTRICITY IS PRODUCED IN POWER PLANTS, WHICH CAN BE :-
1. THERMAL
2.NUCLEAR
3.HYDRAULIC
4. GAS TURBINE
5. GEOTHERMAL
THERMAL POWER PLANTS GENERATE MORE THAN 80% OF THE TOTAL ELECTRICITY PRODUCED IN THE WORLD. FOSSIL FUELS LIKE COAL,FUEL OIL AND NATURAL GAS ARE THE ENERGY SOURCE.
THERMAL, NUCLEAR AND GEOTHERMAL POWER PLANTS WORK WITH STEAM AS THE WORKING FLUID AND HAVE SIMILARITY IN THEIR CYCLE AND STRUCTURE.
CONTINUED…

## Slide 6: CONTINUED…
GAS TURBINE PLANTS ARE GENERALLY USED FOR PEAKING LOAD. THEY ARE BEING INCREASINGLY USED IN CONJUCTION WITH A BOTTOMING STEAM PLANT IN THE MODE OF COMBINED CYCLE POWER GENERATION TO INCREASE COMBINED EFFICIENCY.
HYDRO- POWER PLANTS ARE ESSENTIALLY MULTIPURPOSE. BESIDES GENERATING POWER ,THEY ALSO CATER FOR IRRIGATION.FLOOD CONTROL,FISHERIES,NAVIGATION ETC. HYDROELECTRIC POWER PLANTS HAVE LONG GESTATION PERIOD AND EXPENSIVE.

## Slide 7: CONTINUED…
IT IS FOUND THAT THE DEMAND FOR ELECTRICITY BEARS A LINEAR RELATIONSHIP WITH THE GROSS NATIONAL PRODUCT (GNP) OF A COUNTRY.
PROJECTION OF FUTURE DEMAND OF ELECTRICITY IS TIED WITH ECONOMIC GROWTH OF CONCERNED REGION.
WITH THE INCREASE IN ECONOMIC GROWTH , THE CONSUMPTION OF ELECTRICITY
ALSO INCREASES.
ECONOMIC GROWTH IN INDIA IS DEPENDENT ON THE POWER SECTOR.
THIS HAS LED TO AN ENORMOUS GROWTH IN ELECTRICITY DEMAND OVER
THE LAST TWO DECADES.

## Slide 8: THE POWER SECTOR IN INDIA UNDER THE [VII th ] SCHEDULE OF THE INDIAN CONSTITUTION POWER SECTOR IS ON “CONCURRENT LIST”
CERC
CENTRE
REGULATORY FUNCTION
SERCs
STATES

## Slide 9: Central, State and Private utilities have a complementary role for optimal development of power sector in india
GENERATION
TRANSMISSION
DISTRIBUTION
POWER TRADING: PTC, NVVN
FINANCING: PFC, REC

## Slide 10: Restructuring the SEBs
EARLIER STRUCTURE
(VERTICALLY INTEGRATED)
GENERATION
TRANSMISSION
DISTRIBUTION
A VERTICALLY INTEGRATED ENTITY RESPONSIBLE FOR ALL THE ACTIVITIES THEREBY LEADING TO HIDDEN INEFFICIENCIES ACROSS THE CHAIN
END USERS

## Slide 11: NEW STRUCTURE (UNBUNDLED)
SEB
GENERATION
TRANSMISSION
DISTRIBUTION
3 SEPARATE CORPORATE IDENTITIES

## Slide 13: INDIAN POWER SECTOR- EVOLUTION
 1947 -
 1948 -
Total installed capacity of only 1362 MW.
Electricity Supply Act leads to formation of SEBs
Priority in development through SEBs
Development through Five Year Plans
Emphasis on hydel power in the first two Plans
1966-67 – REBs formed to take care of interstate imbalances
Early Seventies - Country faces unprecedented power crisis
 Capacity: 16,664 MW in 1974
 1975 -
 1991 -
 1992 -
NTPC and NHPC set up in Central Sector Liberalisation; Private participation permitted
 1998 -
 2003 -
Power Grid Corp. formed to facilitate formation of
Grid
Regulation through formation of CERC/SERC Electricity Act’2003

## Slide 14: LEGISLATIVE/ADMINISTRATIVE INITIATIVE TAKEN BY GOVERNMENT TO IMPROVE THE HEALTH OF POWER SECTOR
One time settlement scheme for outstanding dues of CPSUs
National Electricity Policy -2005
Tariff Policy –2006
Integrated Energy Policy 2006
New Hydro Policy –2008
Accelerated Power Development and Reforms Programme – APDRP. It was started in the year 2002-03 for reduction of AT&C losses which was 33%.
Rural Electrification – RGGVY It was started in 2005 and is dedicated to provide electricity to all rural households.
National Mission for Enhanced Energy Efficiency under National Action Plan for Climate Change. 9

## Slide 15: CONTINUED…
2014 - Electricity (Amendment) Bill, 2014 to segregate retail supply from distribution, and bring in multiple supply licensees.
2015- 2017 - As of March 2015, the state discoms had accumulated losses of approximately Rs 3.8 lakh crore and outstanding debt of approximately Rs 4.3 lakh crore. The Ujwal Discom Assurance Yojana (UDAY) was introduced to allow states to help the discoms by taking over their debt.
2017 to Till now- India declared as a power surplus country. All villages have been electrified. New household electrification scheme, Saubhagya, launched. Draft amendments to the 2003 Act propose to segregate the network and supply business, and introduce a system of direct benefit transfers with regard to subsidies. Coal linkages are being allocated through auction (SHAKTI). This scheme was introduced by coal ministry in 2017.It allows for fuel supply agreement with LOA holders ,ensuring coal supply to power plants.
The Electricity Amendment Bill 2022 introduced in Loksabha on 8TH August,2022 and amended Electricity Act 2003. It allows multiple distribution Licensees (DICOMS) to operate in same area of supply.
10

## Slide 16
BACKGROUND
 Three erstwhile Acts that regulated the electricity sector:
The Indian Electricity Act, 1910
The Electricity (Supply) Act, 1948
The Electricity Regulatory Commissions Act, 1998

## Slide 17
BACKGROUND
The Indian Electricity Act, 1910
Provided basic framework for electric supply industry in India.
Growth of the sector through private licensees. Licence by State Govt.
Provision for license for supply of electricity in a specified area
Legal framework for laying down of wires and other works.
Provisions laying down relationship between licensee and consumer.
The Electricity (Supply) Act, 1948
Mandated creation of SEBs.
Need for the State to step in (through SEBs) to extend electrification (so far limited to cities) all across the country

## Slide 18
BACKGROUND
Main amendments to the existing Acts
Amendment in 1975 to enable generation in Central sector
Amendment to bring in commercial viability in the functioning of SEBs .
Section 59 amended to make the earning of a minimum return of 3% on fixed assets a statutory requirement (w.e.f 1.4.1985).
Amendment in 1991 to open generation to private sector and establishment of RLDCs

## Slide 19
BACKGROUND
The Electricity Regulatory Commissions Act, 1998
Provision for setting up of Central/ State Electricity Regulatory Commission with powers to determine tariffs.
Constitution of SERC optional for States.
Distancing of Govt from tariff determination.

## Slide 20: SECTOR WISE GENERATION TARGET OF GOVERNMENT OF INDIA
The electricity generation target (Including RE) for the year 2024-25 has been fixed as 1900 Billion Unit (BU). i.e. growth of around 9.3 % over actual generation of 1738.828 BU for the previous year (2023-24). The generation during 2023-24 was 1738.828 BU as compared to 1624.465 BU generated during 2022-23, representing a growth of about 7.04%.
BREAK-UP CURRENT FINANCIAL YR GENERATION TARGET
1444.943 BU Thermal;
147.709 BU Hydro;
55.348 Nuclear; and
8.000 BU Import from Bhutan.
244.00 BU RES (Excluding Large Hydro)

## Slide 21: Installed Generation Capacity (Sector wise) as on 28.02.2025
100%

## Slide 22: Installed Generation Capacity (Fuel wise) as on 28.02.2025 :

## Slide 23: The annual growth in generation during recent years is as under:
* Provisional up to February,2025

## Slide 24: Total Generation and growth over previous year in the country during 2009-10 to 2024-25
Year | Total Generation (Including Renewable Sources) (BU) | % Growth
2009-10 | 808.498 | 7.56
2010-11 | 850.387 | 5.59
2011-12 | 928.113 | 9.14
2012-13 | 969.506 | 4.46
2013-14 | 1,020.200 | 5.23
2014-15 | 1,110.392 | 8.84
2015-16 | 1,173.603 | 5.69
2016-17 | 1,241.689 | 5.80
2017-18 | 1,308.146 | 5.35
2018-19 | 1,376.095 | 5.19
2019-20 | 1,389.102 | 0.95
2020-21 | 1,381.855 | -0.52
2021-22 | 1,491.859 | 7.96
2022-23 | 1,624.465 | 8.89
2023-24 | 1,739.091 | 7.06
2024-25 * | 1,667.605 | 4.89
* Upto February, 2025 (Provisional), Source : CEA

## Slide 25: The PLF in the country (Coal & Lignite based) from 2009-10 to 2024-25 is as under
* Up to February, 2025 (Provisional), Source : CEA

## Slide 26: The power supply position in the country during 2009-10 to 2024-25
* Upto February, 2025 (Provisional), Source : CEA

## Slide 27
0
2009-10
2023-24
2016-17

## Slide 28
2009-10
2023-24

## Slide 29: Projected Capacity Requirement
2007
2012
2022
2032
Source: Integrated Energy Policy GOI
132 GW
220 GW
425 GW
778 GW
Large Capacity addition required to meet the demand
24

## Slide 30: Ultra Mega Power Projects (UMPP) initiative
An initiative of MOP along with CEA & PFC for development of Coal based environment friendly Ultra Mega Power Projects as pit head stations & coastal stations, each with a capacity of about 4000 MW using super critical technology.
To be awarded to developers on the basis of tariff based competitive bidding guidelines issued by MoP.
The Competitive Bidding process and project development work to be undertaken by wholly owned subsidiaries (Shell Companies/SPVs) established by Power Finance Corporation.
Developers to take up projects on BOO (Build, Own and Operate) basis.
Mega Power benefits available to UMPPs.
Expenditure incurred by shell company in developing the project to be recovered from the selected developer.
25

## Slide 31
Initially following nine (9) numbers Ultra Mega Power Projects (UMPPs) were proposed to be set up in different states:
Sasan UMPP in Madhya Pradesh - coal pithead
Mundra UMPP in Gujarat- coastal
Krishnapatnam UMPP in Andhra Pradesh - coastal
Tilaiya UMPP in Jharkhand- coal pithead
UMPP in Chhattisgarh- coal pithead
Bedabahal UMPP in Odisha - coal pithead
Cheyyur UMPP in Tamil Nadu - domestic coal based
UMPP in Maharashtra- coastal
UMPP in Karnataka - coastal
CONTINUED…

## Slide 32
  STATUS OF UMPPs
1. UMPPs Operational:
Four UMPPs namely Sasan in Madhya Pradesh, Mundra in Gujarat, Krishnapattnam in Andhra Pradesh and Tilaiya in Jharkhand were transferred to the identified developers. Out of the four awarded UMPPs, two UMPPs namely Mundra UMPP and Sasan UMPP are in operation. A brief detail of operational UMPPs is as below:
a)Mundra UMPP in Gujarat: The project was handed over to the successful Bidder i.e. Tata Power Company Ltd., on 23.04.2007 at the evaluated levelized tariff of Rs. 2.26367/kWh. Mundra UMPP is fully commissioned.
b)Sasan UMPP in Madhya Pradesh: The project was handed over to the Successful Bidder i.e. M/s Reliance Power Ltd., on 07.08.2007 at the evaluated levelised tariff of Rs. 1.19616/kWh. Sasan UMPP is fully commissioned.

## Slide 33: Coal is the only proven source of domestic fuel for long term power generation
COAL
Proven reserves
:
~ 106 Billion Tonnes
LIGNITE
Proven reserves
:
36 Billion Tonnes
country for at least next 25-30 years
Natural Gas
Proven Reserves : 1100 BCM
77% domestic Production is used for Power Generation
Coal is going to be the main stay of power generation in the
26

## Slide 36
CONTRIBUTION OF PRIVATE SECTOR

## Slide 37
STRUCTURE OF POWER SECTOR

## Slide 38
FINANCIAL SICKNESS OF SEBs
Indian power sector operated in a monopolistic environment where decisions were not always taken on a commercial basis.
SEBs have long been caught in a vicious circle of shortage of resources and poor operational and financial performances due to:-
a. Politicized irrational tariff structure.
b. High T & D losses mainly due to theft in collusion with SEB employees c. Overstaffing.
d. Poor collection efficiencies.
e. Billing errors.
f. High auxiliary consumption and low PLF of thermal power plants.

## Slide 39
POWER LINES CONDITION BEFORE
POWER LINES CONDITION NOW

## Slide 40
Exhibit 3
SEBs ARE IN A VISCIOUS CYCLE OF UNDER PERFORMANCE
Poor perception of potential value and
protectionist political environment leads to reluctance to change
Poor financial health and near bankruptcy
Leads to inability to abstract capital for future investments &
growth
Continuously tightening
noose of bankruptcy
Poor operational and customer service record
due to lack of performance monitoring
Source: Press searches and McKinsey analysis
16

## Slide 41
NEED FOR THE NEW LEGISLATION
•
Requirement of harmonizing and rationalizing the provisions in the existing laws to
-
Create competitive environment which will result in enhancing
quality and
reliability of service to consumer.
-
distancing regulatory responsibilities of Govt.
•
Obviating need for individual States to enact their own reform laws.
•
Requirement of introducing newer concepts like power trading, open access, Appellate
Tribunal etc.
•
Special provision for the Rural areas.
17

## Slide 42
Click to edit Master title style
ELECTRICITY ACT 2003
• The Act creates a liberal and progressive framework for power sector development
• It facilitates investment by creating competitive environment, and reforming distribution segment of power industry
• Entry barriers removed/reduced :-
• Generation de - licensed, freed from all controls for thermal, with some checks for hydro
•Freedom to captive generation including group captive
•Recognizes trading as an independent activity
•Mandates open access in transmission
…Contd
18

## Slide 43
Click to edit Master title style
ELECTRICITY ACT 2003
•Open access to consumers above 1 MW within five years commencing from 27th Jan 2004 (date of enforcement of amendment to Electricity Act)
•Permits multiple licensees in distribution for same area
•Regulatory Commissions - to develop market (including trading)
Copyright © 2016 Your Company All Rights Reserved.
19

## Slide 45
Copyright © 2016 Your Company All Rights Reserved.
22
PRESENT SCENARIO
POWER CONSUMPTION PATTERN IN INDIA

## Slide 46
C

## Slide 49
CONTINUED…

## Slide 56
NUCLEAR POWER PLANT

## Slide 60
Nuclear Power Development around the World in 2017
● There were 448 operational nuclear power reactors in the world at the end of 2017, with a total net installed power capacity of 392 GW(e).
● An additional 59 units with a total capacity of 60 GW(e) were under construction.
● During 2017, four new nuclear power reactors with a total capacity of 3373 MW(e) were connected to the grid, and five reactors with a total capacity of 3025 MW(e) were retired. In 2017, construction began on four new units that are expected to add a total capacity of 4254 MW(e).
● Electricity generation from operational nuclear reactors increased about 1% in 2017, reaching 2503 TW∙h.
● Nuclear power accounted for about 10% electricity production in 2017
THE NUCLEAR POWER OPTION
Source from IAEA

## Slide 61
 | 61
Environmental Benefits of Nuclear Energy | 
Little or no harmful emissions
Requires less fuel to produce same amount of energy
Less land area to produce same amount of energy
Waste isolation
Zero risk of large scale oil spills
Protection of Salmon Habitat

## Slide 62
 | 62
The Nuclear Power Advantage | 
Highly Concentrated Source of Energy
  1 kg wood: 1 kW·h
  1 kg coal: 3 kW·h
  1 kg oil: 4 kW·h
  1 kg uranium: 50000 kW·h
(3500000 kW·h with reprocessing)

## Slide 63: Operation of a 1000 MW(e) plant will require each year:
 | 63
Advantages of Concentrated Source | 
Coal:
2 6,00 000 t coal (2000 train rake of1300 t each)
Oil:
2 000 000 t oil (10 supertankers)
Uranium:
30 t uranium (One Truck Load)

## Slide 64
 | 64
Nuclear Power: a Compact Source | 
Typical Fossil and Nuclear sites: 1–4 km²
Solar thermal or photovoltaic (PV) parks: 20–50 km² (a small town)
Wind fields: 50–150 km²
Biomass plantations: 4000–6000 km² (a province)

## Slide 65
 | 65

## Slide 66
Open and closed Nuclear Cycles | 
FRESH
FUEL
RECYCLED FUEL FABRICATION
REPROCESSING
REFINING
(U & Th CONCT.)
235U
ENRICHMENT
NUCLEAR POWER PLANT
SPENT FUEL
WASTE CONDITIONING
MINING U & Th
ORES
CLOSED CYCLE
OPEN CYCLE
WASTE DISPOSAL
U238
Th232, U233, Pu239
FISSION PRODUCTS
ENERGY
42

## Slide 67
 | 67
Less sensitive to Fuel Costs | 
The capital costs of nuclear power are higher (about 30%) than that of coal based power. Fuel costs are lower and thus nuclear power is less sensitive to fuel price fluctuations.

## Slide 68: Safety—Three Mile Island, Chernobyl
 | 68
Opposition to Nuclear Power | 
Terrorism—nuclear technology in the wrong hands
Hazardous Waste, storage, and transport
Expensive (maybe, the Study still on that one)

## Slide 69
 | 69
Nuclear Power in India | 
India is outside the Nuclear Non-Proliferation Treaty, it has been for 34 years excluded
from trade, hampered its development of civil nuclear energy.
Lack of indigenous uranium, India has been developing a nuclear fuel cycle to exploit its reserves of thorium.
From 2008, foreign technology and fuel are expected to boost India's nuclear power plans considerably.

## Slide 70
 | 70
Nuclear Reserves of India | 
Atomic Energy Act, 1962, explicitly prohibits Uranium Corporation from making the details public.
However reserves have been estimated to be 60- 70 thousand tonnes.
With the available uranium reserves around 12,000 MW can be generated for 30 years.
India has huge Thorium Deposits-of 25% of world’s deposits.

## Slide 71
 | 71
INDIA’s
THREE STAGE NUCLEAR POWER PROGRAMME
Pressurized heavy water reactor
Breeder reactor produces more
Fissionable material than it consumes to generate energy. This type of reactor is designed to extend the nuclear fuel supply for power generation
FBR NUCLEAR REACTOR USES FAST NEUTRON TO GENERATE MORE NUCLEAR FUELS THAN THEY CONSUME WHILE GENERATING POWER
Th =U232
Pu = U239

## Slide 73
CONTINUED…

## Slide 76
Click to edit Master title style
Copyright © 2016 Your Company All Rights Reserved.
8

## Slide 77
FUTURE PLAN OF GOI FOR POWER
DEVELOPMENT IN INDIA
The Government of India's future plans for power generation focus on a significant transition towards renewable energy sources, aiming for 500 GW of non-fossil fuel capacity by 2030 and a 50% decarburization of energy by 2030.
This includes initiatives like the National Green Hydrogen Mission, PM-KUSUM, and PM Surya Ghar, along with schemes for domestic solar PV module manufacturing.
With a commitment to achieving 500 GW of non-fossil fuel-based energy capacity by 2030, India is emerging as a global leader in clean energy.
As on 20th Jan 2025, India's total non-fossil fuel based energy capacity has reached 217.62 GW.

## Slide 78
ROLE OF NTPC IN POWER DEVELOPMENT IN INDIA

## Slide 79
INTRODUCTION
NTPC is India’s largest energy conglomerate with roots planted way back in 1975 by GOI to accelerate power development in India. Since then it has established itself as the dominant power major with presence in the entire value chain of the power generation business.
From fossil fuels it has forayed into generating electricity via hydro, nuclear and renewable energy sources. This foray will play a major role in lowering its carbon footprint by reducing green house gas emissions. To strengthen its core business, the corporation has diversified into the fields of consultancy, power trading, training of power professionals, rural electrification, ash utilization and coal mining as well.
IPO in 2004
FPO in 2010
NTPC became a Maharatna company in May 2010.
As of December, 2023, there are 13 Maharatnas CPSEs in India.
NTPC is ranked No. 2 Independent Power Producer(IPP) in Platts Top 250 Global Energy Company rankings

## Slide 80
NTPC has policy to have diversified fuel mix and by Year 2032, non fossil fuel based generation capacity shall make up nearly 30% of NTPC,s portfolio.

## Slide 82
CONTINUED…

## Slide 83
REGINAL SPREAD OF GENERATION FACILITIES OF NTPC PLANTS

## Slide 84
C
77,461.5

## Slide 85
C
60

## Slide 86
FUTURE CHALLENGES OF
POWER SECTOR

## Slide 87
Limitations in Project Management Capabilities.
Timely availability of raw materials and inputs such as turbine forgings.
Limited vendors for Balance of Plant equipment.
Availability of adequate number of young and talented manpower in Power Sector.
Availability of gas at reasonable prices

## Slide 88
CRITICAL ASPECTS
Areas which could affect target achievement:-
Power Plant Equipment
Timely and Adequate Supply of key input materials including Fuel
Technology
Construction and Erection Agencies
Infrastructure development
Manpower training and development
Financial Resources

## Slide 89
POWER PLANT EQUIPMENTS
Need to substantially augment equipment manufacturing.
Outsourcing of equipment manufacturing on system basis
to ancillary units.
The supplier and construction agency for the project should be monitored in terms of “MW Commissioned”.
More suppliers for Balance of Plant equipment are essential.
Plant wise plans for hiring various construction equipment like Crane etc.

## Slide 90
KEY INPUT MATERIALS
Shortage of Special materials such as CRGO (Cold –rolled grain–oriented) Steel, castings and forgings for Turbine Generators/Transformers due to international demand.
Indigenous manufacturing capacity of CRGO should be created at the earliest.
Advance procurement of the material
Adequate fuel availability

## Slide 91
TECHNOLOGY
Need to set up efficient power plants in terms of conversion and environment.
Transfer and indigenization of super critical technology.

## Slide 92
CONSTRUCTION & ERECTION AGENCIES
More construction and erection agencies to be attracted to the power sector.

## Slide 93
Manpower Training and Development
Shortage of skilled Engineers and Managers.
Skilled manpower for HP Welding, Aluminum Welding, Cable jointing, Crane Operation etc.
Training facilities for Engineers, Projects Managers and other skilled manpower.

## Slide 94
STRINGENT ENVIRONMENTAL NORMS

## Slide 95
NOTIFICATION FOR THERMAL POWER PLANTS
INDUSTRY | PARAMETER | PROPOSED STANDARDS | CURRENT STANDARDS
TPSs Units Installed before 31, December, 2003 | Particulate matter | 100 mg/Nm3 | 150 mg/Nm3
 | Sulfur Dioxide (SO2) | 600 mg/Nm3( Units smaller than 500MW capacity units) | No statutory Limits
 | Oxides of nitrogen (NOx) | 600 mg/Nm3 | No statutory Limits
 | Mercury (Hg) | 0.03 mg/Nm3 | No statutory Limit

## Slide 96
NOTIFICATION FOR THERMAL POWER PLANTS
INDUSTRY | PARAMETER | PROPOSED STANDARDS | CURRENT STANDARDS
TPSs Units Installed after 2003 to December 31, 2016 | Particulate matter | 50 mg/Nm3 | 100 mg/Nm3
 | Sulfur Dioxide (SO2) | 200 mg/Nm3( For Units having capacity of 500 MW and above ) | No statutory Limits
 | Oxides of nitrogen (NOx) | 300 mg/Nm3 | No statutory Limits
 | Mercury (Hg) | 0.03 mg/Nm3 | No statutory Limit

## Slide 97
Greenhouse Gas Emissions
58% of the total emissions come from the energy sector.
These include emissions from burning of traditional bio-mass fuels, coal mining and fugitive emissions oil and natural gases.
Power plant industry is next big contributor at 22% with cement industry being one of major contributor.
Agricultural sector contributes 17% of GHG emissions. The emissions under agricultural sector include those from enteric fermentation in domestic animals, manure management, rice cultivation and burning of agriculture residues.

## Slide 98
INTEGRATION OF SOLAR ENERGY WITH GRID
As the proportion of Solar energy supply to grid becomes larger ,it will start impacting the grid parameters.
At day time there thermal power plants will have to run on partial loading because solar energy will be available, thus adversely impacting the efficiency/stability of thermal plant.

## Slide 99
Copyright © 2016 Your Company All Rights Reserved.
37

## Slide 100
THANKING YOU
ANY SUGGESTION & COMMENT

## Slide 101
WHAT IS CAGR?
It is annualized average rate of revenue growth between two given years, assuming growth takes place at an exponentially compounded rate.
CAGR, year X to year Z = [(value in year Z/value in year X) ^ (1/N)-1] For example, the CAGR for 2006 to 2011 is calculated as: CAGR, 2006 to 2011 (X = 2006, Z = 2011, N = 5) = [(value in 2011/value in 2006) ^ (1/5)-1]

## Slide 102
NTPC is not only the foremost power generator; it is also among the great places to work. The company is guided by the “People before Plant Load Factor” mantra which is the template for all its human resource related policies. In 2019, NTPC is recognized as “Laureate” for consistently ranking among “Top 50 Best Companies to Work for in India” for last 11 years in the Great Place to Work and Economic Times survey. Besides, NTPC was also recognized as the best among PSUs and in Manufacturing.

## Slide 103
C
45

## Slide 104
GNP:-
The total value of goods produced and services provided by a country during one year, equal to the gross domestic product plus the net income from foreign investments.
GNP
Gross National Product takes into account the manufacturing of tangible goods such as vehicles, agricultural products, machinery, etc., as well as the provision of services like healthcare, business consultancy, and education. GNP also includes taxes and depreciation.
OR
Gross National Product (GNP) is the total value of all finished goods and services produced by a country's citizens in a given financial year, irrespective of their location. GNP also measures the output generated by a country's businesses located domestically or abroad.
GNP

## Slide 105
FUTURE PLAN OF GOI FOR POWER
DEVELOPMENT IN INDIA
The year 2024 saw a record-breaking 24.5 GW of solar capacity and 3.4 GW of wind capacity added, reflecting a more than twofold increase in solar installations and a 21% rise in wind installations compared to 2023.
This surge was driven by government incentives, policy reforms, and increased investments in domestic solar and wind turbine manufacturing.
Solar energy remained the dominant contributor to India’s renewable energy growth, accounting for 47% of the total installed renewable energy capacity.

## Slide 106
The Three Mile Island accident was a partial nuclear meltdown of the Unit 2 reactor (TMI-2) of the Three Mile Island Nuclear Generating Station, located on the Susquehanna River in Londonderry Township, near Harrisburg, Pennsylvania.
The reactor accident began at 4:00 a.m. on March 28, 1979, and released radioactive gases and radioactive iodine into the environment. It is the worst accident in U.S. commercial nuclear power plant history. On the seven-point logarithmic International Nuclear Event Scale, the TMI-2 reactor accident is rated Level 5, an "Accident with Wider Consequences".
The accident began with failures in the non-nuclear secondary system, followed by a stuck-open pilot-operated relief valve (PORV) in the primary system, which allowed large amounts of water to escape from the pressurized isolated coolant loop.
The mechanical failures were compounded by the initial failure of plant operators to recognize the situation as a loss-of-coolant accident
THREE MILE ISLAND ACCIDENT

## Slide 107
The Chernobyl disaster, a Level 7 nuclear accident, occurred on April 26, 1986, at the Chernobyl Nuclear Power Plant in Ukraine, resulting in a massive release of radioactive material into the environment.
On 26 April 1986, the No. 4 reactor of the Chernobyl Nuclear Power Plant, located near Pripyat, Ukrainian SSR, Soviet Union (now Ukraine) exploded.
It was the result of a flawed reactor design that was operated with inadequately trained personnel. The resulting steam explosion and fires released at least 5% of the radioactive reactor core into the environment, with the deposition of radioactive materials in many parts of Europe.
CHERNOBYL DISASTER IN UKRAINE